## Slide 1: UNIT 2
UNIT II - NATURAL DISASTER
10

## Slide 2
10

## Slide 3
10

## Slide 4
10

## Slide 5: Earthquakes
Vibrations induced in the earth’s crust due to internal or external causes that virtually shake up a part of the crust and all the structures and living and non- living things existing on it.
Strongest, Quickest and most
unexpected natural calamities.
10

## Slide 6: Earthquake
10
An earthquake is the result of a sudden release of energy in Earth's crust that creates seismic waves.
Seismic activity of an area refers to the frequency, type & size of earthquakes experienced over a period of time & are measured using seismometers.
At the Earth's surface, earthquakes manifest themselves by shaking & sometimes displacement of the ground.

## Slide 7: Study of Earthquake
10
Ascertain the factors that lead to earthquake
Predict the occurrence of an earthquake
Design and Provide structures that will protect during an earthquake

## Slide 8
10

## Slide 9: Earthquakes
10
The vibrations that are set up when an earthquake takes place are propagated as a number of different types of waves. Different types of seismographs are designed to record these waves. A major shock is recorded by seismographs all over the world, and its epicentre, time of origin, depth of focus, magnitude etc. can be worked out from these records called seismograms.
Of the various types of waves set up by an earthquake the most important are i) P primary waves, which are the fastest. ii) S waves or secondary waves which are slower and iii) L or long wave which arrive at a station later than P & S wave as they follow zig zag path.

## Slide 10: Earthquakes
Fastest wave
Helps in understanding the core
10

## Slide 11: Magnitude
10
Rating of an Earthquake on the basis of amplitude of seismic waves.
Charles F. Richter in 1935 – Scale of Magnitude.
Richter Magnitude is the logarithm of the maximum seismic wave amplitude at a distance of 100 km from the epicenter.
M = log A – log A0
Magnitude Scale – Mb and Ms
Ms : Shallow earthquake and Mb : Stronger and wide spread earthquake

## Slide 12: Intensity
10
Rating of an Earthquake on the basis of its effects on living and non-living things.
Degree of shacking.
Building collapse; Landslide triggered; river changes course; land may burst open.
Scales for seismic Intensity Rossi Forrel (Rossi in 1883)
and Mercalli scale (1902)- M.M.Scale.
Intensity is indicated as a set of whole number.

## Slide 13
10

## Slide 14: Isoseismals
Hypothetical lines – Same
Intensity
A line joining all the similar intensity points are known as Isoseismals.
Isothermal Records.
Factors controlling Isoseismals
  Nature of Shocks – Shallow
Isoseismals;
origin give rise to
Deep
high
origin
produce moderate Isoseismals.
Nature of Rocks – Uniform nature (Isoseismals is regular and circular) - Structural and lithological variations (Isoseismals is irregular and elliptical in shape).
14

## Slide 15: Classification of Earthquake
15
Depth of focus
  Shallow – upto 60km
  Intermediate – between 60 and 300
km
  Deep seated – between 300 and 700 km
Causes of origin
  Tectonic Earthquake – faulting of blocks of the crust along rupture plane.
  Non-Technotic Earthquake – volconic eruption, atomic explosions, landlsides and subsidence.
3. Magnitude
Class | Magnitude
A | 7.8 and above
B | 7.0 – 7.7
C | 6.0 – 7.0
D | 5.3 – 6.0
E | Less than 5.3

## Slide 16: Causes of Earthquake
1. Non-tectonic Causes
Volcanic eruptions – forceful eruption of lava
Atomic Explosions
Collapse (Collapse Earthquakes) of ground by natural or artificial cause – Local nature and rare occurrence.
Severe local tremors are caused by huge landslides, rock bursts.
15

## Slide 17: Causes of Earthquake
2. Tectonic Earthquakes
Displacement of blocks along fractures called faults.
Elastic Rebound Theory (H.F.Reid 1906).
Rocks behave as elastic masses.
As the first reaction, when these are stressed, the rocks respond to bend.
The elastic limit may be reached and rupture may develop along with displacement of blocks.
15

## Slide 18: Causes of Earthquake
15
2. Tectonic Earthquakes
Displacement is associated with a rebound of curvature
developed due to bending during stressing.
Most of the elastic energy is released at the place of focus in
the form of energy waves.
1. First – the preparatory process; Non-Hydrostatic stress; ‘Foreshocks’ are observed.
2. Second – The rupture phase. The stored elastic energy released and transformed into potential energy. ‘Main shock’
3. Third– the post failure
adjustment.
‘after shocks’ as a residual strain from rock bodies.

## Slide 19: Causes of Earthquake
15
3. Reservoir Associated Earthquake
Impounding water in Reservoir.
Aseismic region experiences Earthquake.
Cause
Sagging Effect of the land – when the rock of the basin bear
additional load by impound water, it starts bending – stress
and redistribution in the region. Readjustment triggers seismic shocks.
Increased pore pressure– Increment of pore pressure has an
adverse effect on the shearing strength of the basin rocks which may lead to failure and slippage.

## Slide 20: Plate Tectonics and Earthquakes
The Earth’s crust is divided into 12 major plates which are moved in various directions.
The plates collide, pull apart, or scrape against each other.
Each motion causes different types of features on the Earth’s crust.
The word, tectonic, refers to changes in the crust because of plate interaction.
15

## Slide 21: What are tectonic plates made of?
Plates are made of rigid lithosphere.
15

## Slide 22
Plate Movement
“Plates” of lithosphere are moved around by the underlying hot mantle convection cells
15

## Slide 23
Earthquakes occurs along the boundaries of the plates.
Thrust faulting and block faulting.
Divergent – rise in molten material (sub-oceanic ridges ex.volcanism).
Convergent – subduction of one plate under another plate (Faulting + displacement)
  Divergent
Convergent
Transform
23

## Slide 24
24

## Slide 25: Effects of Earthquake
24
Primary Effect – Related to the cause of origin of an Earthquake. Tectonic Earthquakes – geological structures.
Secondary Effect – related to passage of seismic waves and associated shaking motion of the ground. It is observed on constructions of all types. Landslides are triggered; standing structures are collapsed; Tsunamis; trees are uprooted; loose objects are thrown away.

## Slide 26: Recording an Earthquake
24
Earthquake may be the result of combined action of
Release of elastic energy
Propagation of the seismic waves through the ground
Acceleration of the ground.

## Slide 27: Seismographs
Instrument designed to record the earth motion by seismic waves is
called Seismographs.
Seismogram? Horizontal and Vertical?
PENDULUM
27

## Slide 28: Seismogram
Seismograph - Ground Acceleration, Ground Velocity and ground
displacement

## Slide 29: Travel time Records
Marked difference in the velocities of P, S and L waves.
Travel time curve
The distance of the epicenter and time of the origin can be calculated.

## Slide 30: Location of Epicenter
S-P travel time curve
From Isoseismals

## Slide 31: Distribution of Earthquake
Shocks of the past confined with two large geographical belts
The Circum-Pacific belt
The Mediterranean Belt

## Slide 32: Seismic History
Seismic events w.r.t Intensity and Magnitude.
The heavily populated regions are classified into seismically zones and sub-zones.
Seismic zonation – Qualitative records and geological setting of the area. Extrapolations and computations are required.
Microzonation – Actual seismic data used.
Facilitates the job of an engineer to decide the type of construction.

## Slide 33: Earthquake Zoning of India

## Slide 34: Earthquake Zoning of India

## Slide 35: Earthquake Zoning of India
Zone 5
Zone 5 covers the areas with the highest risks zone that suffers earthquakes. The IS code assigns zone factor of 0.36 for Zone 5. Structural designers use this factor for earthquake resistant design of structures in Zone 5. The zone factor of 0.36 is indicative of effective (zero period) peak horizontal ground accelerations of
0.36 g (36% of gravity) that may be generated during Maximum Considered Earthquake (MCE) level earthquake in this zone. It
is referred to as the Very High Damage Risk Zone. The state of
Kashmir,the western and central Himalayas, the North-East Indian region and the Rann of Kutch fall in this zone.
Generally, the areas having trap or basaltic rock are prone to
earthquakes.

## Slide 36: Earthquake Zoning of India
Zone 4
This zone is called the
Zone. The IS
High Damage Risk
code
assigns zone factor of
0.24 for Zone 4. The Indo-Gangetic basin and the capital of the
country Jammu
(Delhi),
and
Kashmir fall in Zone
4. In Maharashtra Patan area(Koyananager) also in zone 4.

## Slide 37: Earthquake Zoning of India
Zone 3
The
Andaman and
Nicobar Islands, parts of Kashmir, Western Himalayas fall under this zone. This zone is classified as Moderate Damage Risk Zone. The IS code assigns zone factor of 0.16 for Zone 3.

## Slide 38: Earthquake Zoning of India
Zone 2
This region is classified as the Low Damage Risk Zone. The IS code assigns zone factor of 0.10 (maximum horizontal acceleration that can be experienced by a structure in this zone is 10% of gravitational acceleration) for Zone 2.

## Slide 39: Flood
A flood is an overflow of water that submerges land, may occur as an overflow of water from water bodies, such as a river or lake, in which the water overtops, resulting in some of that water escaping it’s usual boundaries or it may occur due to accumulation of rainwater on saturated ground in an areal flood. Floods often cause damage to livelihood & structures.

## Slide 50: Landslide
A landslide is a geological phenomenon that includes a wide range of ground movements, such as rock falls, deep failure of slopes & shallow debris flows. Landslides can occur in offshore, coastal & onshore environments. Although the action of gravity is the primary driving force for a landslide to occur, a landslide often requires a trigger before being initiated.

## Slide 51: Definition
Temporary instability of the mass body such as soil & rock.
These masses may leave their original position gradually or abruptly and start downward movement. These movements resulted in loss of life and property, especially when it occurs near populated areas, along highways, dams & reservoirs or under heavy structures.
Such movements of the superficial masses have been termed as landslides or landslips.
These mass movements highly influence the stability of the Civil Engineering projects.

## Slide 53: Classification
Mass movement are classified according to
Wide variety of geological conditions in which these movements take place.
Heterogeneity in the type of material involved in failure.
Nature of the surface along which the landslide takes place
Speed of the movement.

## Slide 54
The mass movement is divided into three groups on the basis of type of failure
Flowage - A downgrade movement of mass along no definite surface of failure. Mass involved in this type of failure is primarily unconsolidated or loosely packed or rendered so by natural processes of decay and disintegration. The result is that the movement is distributed mass of irregular shape.
Sliding - A true landslide is a type of mass failure in which a superficial mass fails by moving as a whole along a definite surface of failure. The surface of failure may be planar or semicircular in outline. The mass above the failure surface is unstable whereas the material lying below this surface is generally stable. Sliding may involve material of any composition, shape and of varying degree of consolidation.
Subsidence - It is defined as sinking or settling of the ground in a vertically downward direction which may occur because of removal of natural support from the underground or due to compaction of weaker rocks under the loam. The resultant product from this process is artificial hill which suffers sinking Downward movement.

## Slide 55: Causes of Mass movement
Internal Factors – 1. The Nature of Slope, 2. Role of Water, 3. Composition of Mass, 4. Geological Structures
External Factors – 1. vibrations from artificial and natural phenomena. Vibrations due to natural causes such as earthquakes often initiate mass failures on a large scale that may continue much after the quake. 2. Another important external factor, often overlooked, is the removal of the support at the foot of the slope, as during excavation for road widening, without due regards to the critical conditions of the stability. 3. The stresses due to the additional load add to the stresses due to the mass of the slope.

## Slide 56: Monitoring Mass Movements
Continuous monitoring of slope movement is very useful in detecting the symptoms that are indicative of sudden failure of the slope.
The data collected through monitoring system may be of great help in deciding control methods for subsequent failures.
Monitoring of slope can be done by
  Conventional surveying
  Advanced techniques like EDM, Laser equipment, Settlement gauges & extensometers.
  Piezometer (pore water pressure)
  Interferometry

## Slide 57: Controlling Mass Movements
Before deciding the effective measures it is essential to study
The history of a slide area – in order to reveal the areal extent as well as depth upto which the mass is unstable, extent & frequency with which it has failed during a period of time.
This can be done by detailed geotechnical examination of the slide area,
Composition of failing mass
Structural decomposition of the mass
Position of GW table within & around the critical mass
Relation of the mass prone to failure to any surface water body
The slope of the ground

## Slide 58: Mitigation Strategies
Hazard mapping
Retaining walls
Surface drainage control works
Engineered structures with strong foundation
Increasing vegetation cover
Flattening of the slope
Stitching of the debris cover to the rock
Grouting
Geotextiles
Rock fall protection
Mudflow barriers
Debris basins

## Slide 59: Mitigation Measures
Providing Drainage
Construction of Structures
  Retaining Wall
  Gabion Wall
Slope treatment
  Soil nailing
  Rock bolting
  Rock netting
  Vegetation cover
  Geocell

## Slide 60
Construction of Structures
1.Retaining Wall 2.Gabion Wall

## Slide 61: Slope treatment
Soil nailing
Rock bolting
Rock netting
Vegetation cover
Geocell

## Slide 62: Slope treatment
Soil nailing
Rock bolting
Rock netting
Vegetation cover
Geocell

## Slide 63: Avalanche
An avalanche is a rapid flow of snow down a sloping surface. Avalanche is typically triggered in a starting zone from a mechanical failure in the snowpack(slab avalanche) after initiation, avalanches usually accelerate rapidly & grow in mass & volume as they collect more snow.

## Slide 64: Definition
Technically, an avalanche is any amount of snow sliding down a mountainside. It can be compared to a landslide, only with snow instead of earth. Another common term for avalanche is “snowslide”. As an avalanche becomes nearer to the bottom of the slope, it gains speed and power, this can cause even the smallest of snowslides to be a major disaster.

## Slide 65: Types of Avalanches
Surface Avalanche that occurs when a layer of snow with different properties slides over another layer of snow. For example, when a layer of dry loosely packed snow slides over a dense layer of wet snow.
Full-Depth Avalanche which, as it’s name would lead you to believe, occurs when an entire snow cover, from the earth to the surface, slides over the ground.

## Slide 66: 4 Types of Avalanches
Loose Snow Avalanches: First of these are the Loose Snow Avalanches. They are common on steep slopes and are seen after a fresh snowfall. Since the snow does not have time to settle down fully or has been made loose by sunlight, the snow-pack is not very solid. Such avalanches have a single point of origin, from where they widen as they travel down the slope.
Slab Avalanches: Loose Snow Avalanches in turn could cause a Slab Avalanche, which are characterized by a the fall of a large block of ice down the slopes. Thin slabs cause fairly small amounts of damage, while the thick ones are responsible for many fatalities.

## Slide 67: 4 Types of Avalanches
Powder Snow Avalanches: Powder Snow Avalanches are a mix of the other forms, Loose Snow and Slab. The bottom half of this avalanche consists of a slab or a dense concentration of snow, ice and air. Above this is a cloud of powdered snow, which can snowball into a larger avalanche as it progresses down the slope. The speed attained by this avalanche can cross 190 miles per hour and they can cross large distances.
Wet Snow Avalanches: Finally, there are Wet Snow Avalanches. These are quite dangerous as they travel slowly due to friction, which collects debris from the path fairly easily. The avalanche comprises of water and snow at the beginning, but understanding of avalanches has showed us that it can pick up speed with ease.

## Slide 69: Main parts of Avalanche
The starting zone is the most volatile area of a slope, where unstable snow can fracture from the surrounding snow cover and begin to slide. Typical starting zones are higher up on slopes. However, given the right conditions, snow can fracture at any point on the slope.
The avalanche track is the path or channel that an avalanche follows as it goes downhill. Large vertical swaths of trees missing from a slope or chute-like clearings are often signs that large avalanches run frequently there, creating their own tracks. There may also be a large pile-up of snow and debris at the bottom of the slope, indicating that avalanches have run.
The runout zone is where the snow and debris finally come to a stop. Similarly, this is also the location of the deposition zone, where the snow and debris pile the highest.

## Slide 70: Causes of Avalanche
Snowstorm and Wind Direction: Heavy snowstorms are more likely to cause Avalanches. The 24 hours after a storm are considered to be the most critical. Wind normally blows from one side of the slope of mountain to another side. While blowing up, it will scour snow off the surface which can overhang a mountain.
Heavy snowfall: Heavy snowfall is the first, since it deposits snow in unstable areas and puts pressure on the snowpack. Precipitation during the summer months is the leading cause of wet snow avalanches.

## Slide 71: Causes of Avalanche
Human Activity: Humans have contributed to the start of many avalanches in recent years. Winter sports that require steep slopes often put pressure on the snow-pack which it cannot deal. Combined with the heavy deforestation and soil erosion in mountain regions, it gives the snow little stability in the winter months. Further natural causes include earthquakes and tremors, since they can often create cracks in the snowpack.
Vibration or Movement: The use of All Terrain Vehicles and Snowmobiles creates vibrations within the snow that it cannot withstand. Coupled with the gravitational pull, it is one of the quickest ways to cause an avalanche. The other is construction work done with explosives, which tend to weaken the entire surrounding area.

## Slide 72: Causes of Avalanche
Layers of Snow: There are conditions where snow is already on the mountains and has turned into ice. Then, fresh snow falls on top which can easily slide down.
Steep Slopes: Layers of snow build up and slide down the mountain at a faster rate as steep slopes can increase the speed of snow. A rock or piece of huge ice can shake the snow and cause it to come down.
Warm Temperature: Warm temperatures that can last several hours a day can weaken some of the upper layers of snow and cause it to slide down.

## Slide 73: Effects of Avalanches
Damage to Life and Property: A large number of casualties takes place after
avalanches hit heavily populated areas. Infrastructure is damaged and the
blockage caused, impacts the livelihood of many. People who enjoy skiing,
snowboarding and snowmobiling are at a greater risk of losing their lives. A
powerful avalanche can even destroy buildings and power supplies can be cut off.
Flash floods: When an avalanche occurs, it brings down all the debris with it and
can cause havoc in low lying areas. Flash floods are seen to happen after
avalanches, which is a long term problem many villagers and townspeople have
to deal with. They can also change weather patterns and cause crop failure in farms present on the lower fields.
Economic Impact: An avalanche can block anything in its path and even restrict
the normal movement of traffic. Various ski resorts depend on tourists to run
their business successfully. Ski resorts and other businesses are forced to close
until the avalanche decreases and weather conditions become suitable.

## Slide 74: Drought
Drought, lack or insufficiency of rain for an extended period that causes a considerable hydrologic (water) imbalance and, consequently, water shortages, crop damage, stream flow reduction, and depletion of groundwater and soil moisture. It occurs when evaporation and transpiration (the movement of water in the soil through plants into the air) exceed precipitation for a considerable period. Drought is the most serious physical hazard to agriculture in nearly every part of the world.
Drought is caused by not only lack of precipitation and high temperatures but by overuse and overpopulation.

## Slide 75: Categories of Drought
Meteorological drought is specific to different regions, depending on the amount of yearly precipitation that's average for that area. For example, the southwest portion of the United States averages less than 3 inches (7.6 centimeters) of precipitation per year, while the Northwest gets more than 150 inches (381 cm) per year, according to the U.S. Department of Interior. A decrease in precipitation compared to the historical average for that area would qualify as a meteorological drought.
Agricultural drought accounts for the water needs of crops during different growing stages. For instance, not enough moisture at planting time may hinder germination, leading to low plant populations and a reduction in yield.
Hydrological drought refers to persistently low water volumes in streams, rivers and reservoirs. Human activities, such as drawdown of reservoirs, can worsen hydrological droughts. Hydrological drought is often linked with meteorological droughts.
Socioeconomic drought occurs when the demand for water exceeds the supply. Examples of this kind of drought include too much irrigation or when low river flow forces hydroelectric power plant operators to reduce energy production.

## Slide 76: Tracking Drought
In the United States, the Palmer Drought Severity Index (PDSI, weekly index from CPC shown), devised in 1965, was the first comprehensive drought indicator. It is considered most effective for unirrigated cropland. The PDSI combines temperature, precipitation, evaporation, transpiration, soil runoff and soil recharge data for a given region to produce a single negative number that indicates drought conditions.
This index serves as an estimate of soil moisture deficiency and roughly correlates with drought severity. The PDSI is the most commonly used index for drought monitoring and research. It has been widely used in tree-ring-based reconstructions of past droughts in North America and other regions.
In 1999, the U.S. Drought Monitor replaced the PDSI as the nation's drought indicator.
The nationwide Drought Monitor categorizes drought into five levels of severity:
  abnormally dry (category D0, corresponding to a PDSI between -1.0 and 1.9)
  moderate drought (D1, PDSI between -2.0 and -2.9)
  severe drought (D2, PDSI between -3.0 and -3.9)
  extreme drought (D3, PDSI between -4.0 and -4.9)
  exceptional drought (D4, PDSI between -5.0 and -5.9)

## Slide 77: Drought Mitigation Measures
The components of a drought preparedness and mitigation plan are the following:
  Prediction
  Monitoring
  Impact assessment
  Response.
Prediction can benefit from climate studies which use coupled ocean/atmosphere models, survey of snow packs, anomalous circulation patterns in the ocean and atmosphere, soil moisture, assimilation of remotely sensed data into numerical prediction models, and knowledge of stored water available for domestic, stock, and irrigation uses.
Monitoring exists in countries which use ground-based information such as rainfall, weather, crop conditions and water availability. Satellite observations complement data collected by ground systems. Satellites are necessary for the provision of synoptic, wide-area coverage.
Impact assessment is carried out on the basis of land-use type, persistence of stressed conditions, demographics and existing infrastructure, intensity and areal extent, and its effect on agricultural yield, public health, water quantity and quality, and building subsidence.
Response includes improved drought monitoring, better water and crop management, augmentation of water supplies with groundwater, increased public awareness and education, intensified watershed and local planning, reduction in water demand, and water conservation.

## Slide 78: Drought preparedness and mitigation can be accomplished
(1) soil and water conservation
(2) herd management.

## Slide 79: Soil and Water Conservation
Conservation practices minimize the disruption of the soil's structure, composition and natural biodiversity,
thereby reducing erosion and soil degradation, surface runoff, and water pollution. The following are established practices of soil and water conservation
Crop rotation
Contoured row crops
Terracing
Tillage practices
Erosion-control structures
Water retention and detention structures
Windbreaks and shelterbelts
Litter management
Reclamation of salt-affected soil.

## Slide 80: Engineering measures
Engineering measures differ with location, slope of the land, soil type, and
amount and intensity of rainfall. Measures commonly used are the following:
Contour bunds, trenches and stone walls These features prevent soil erosion and obstruct the flow of runoff. The retained water increases soil moisture and recharges the groundwater.
Check dams and other gully-plugging structures Check dams are temporary structures constructed with locally available materials. Types of check dams are the brush-wood dam (Fig. 2 a), the loose-rock dam (Fig. 2 b) and the woven-wire dam.
Percolation ponds These features store water for livestock and recharge the groundwater. They are constructed by excavating a depression to form a small reservoir, or by constructing an embankment in a natural ravine or gully to form an impoundment.

## Slide 81: Moisture-conservation practices
For agricultural crops, measures include ridges and furrows, basins, and water spreading.
For tree crops, measures include saucer basins (Fig. 3), semi-circular bunds, crescent-shaped bunds, catch pits and deep pitting.
Rainwater harvesting collects rainfall or moisture for immediate or eventual use in irrigation or domestic supplies. Part of the rainwater collected from roofs can be stored in a cistern or tank for later use.
Landscape contouring is used to direct runoff into areas planted with trees, shrubs, and turf.

## Slide 82: Cyclone
"Cyclonic Storm" or a "Cyclone" is an intense vortex or a whirl in the atmosphere with very strong winds circulating around it in anticlockwise direction in the Northern Hemisphere and in clockwise direction in the Southern Hemisphere.
Hurricanes, typhoons and cyclones are all rotating storms spawned in the tropics. As a group, they can be referred to as tropical cyclones.
Because of the Coriolis effect, these storms rotate counterclockwise in the Northern Hemisphere and clockwise in the Southern Hemisphere.

## Slide 83: Coriolis effect

## Slide 84: Anticyclones
Defined as a large-scale circulation of winds around
a central region of high atmospheric pressure,
clockwise in the Northern Hemisphere and counterclockwise in the Southern Hemisphere.
Anticyclones are regions of relatively high pressure
on horizontal surfaces, or high geopotential height
on isobaric surfaces, around which air circulates
clockwise in the Northern Hemisphere and counterclockwise in the Southern Hemisphere.
They are an area of high atmospheric pressure where the air is sinking.
The winds may be very light.
In summer, anticyclones bring dry, hot weather. In winter, clear skies may bring cold nights and frost.

## Slide 87: Types of Cyclone
Classification of cyclone according to synoptic scale
Polar cyclone (polar regions, vast)
Polar lows (polar regions, short)
Extratropical cyclone (mid-latitude cyclone)
Subtropical cyclone (between the equator and 50o N and S)
Mesocyclone (associated with tornado formation)
Tropical cyclone (tropics)

## Slide 89: Distribution of cyclones

## Slide 93: Surge prone coasts of India
Storm surge heights depend on the intensity of the cyclone, i.e., very high-
pressure gradient and consequent very strong winds and the topography of
seabed near the point where a cyclone crosses the coast. Sea level also rises due
to astronomical high tide. Elevation of the total sea level increases when peak surge occurs at the time of high tide.
Cyclones that struck the coasts of India
Rameswaram Cyclone of 17th to 24th December 1964 wiped out Dhanuskodi in Rameswaran Island from the map.
Bangla Desh Cyclone of 8-13 November 1970 toll of about 3,00,000 people.
Andhra Cyclone of 14-20 November 1977 that crossed coast near
Nizampatnam in the evening of 19th, took a toll of about 10,000 lives.
The West coast of India is less vulnerable to storm surges than the east coast of India in terms of both the height of storm surge as well as frequency of occurrence. However, the following segments are vulnerable to significant surges :
i) Maharashtra coast, north of Harnai and adjoining south Gujarat coast and the coastal

## Slide 95: Destruction caused by Cyclones
Consequent strong winds. These, in turn, generate storm surges.
Abnormal rise of sea level near the coast caused by a severe tropical cyclone.
Very strong winds may damage installations, dwellings, communication systems, trees., etc. resulting in loss of life and property.
Heavy rains due to cyclones may cause river floods

## Slide 96: PROTECTION AGAINST CYCLONE
Four Stage Warning
De-warning – message is issued when the Tropical Cyclone weakens into Depression State.
STAGE | STAGE OF WARNING | TIME
First Stage | PRE CYCLONE WATCH | Before 72hrs
Second Stage | "CYCLONE ALERT" | Before 48hrs
Third Stage | CYCLONE WARNING | Before 24hrs
Fourth Stage | POST LANDFALL OUTLOOK | Before 12hrs

## Slide 97: Cyclone Operation in India
Cyclone warnings are provided by IMD from the Area Cyclone Warning Centres (ACWCs) at Calcutta, Chennai and Mumbai and Cyclone Warning Centres (CWCs) at Bhubanes-war, Visakhapatnam and Ahmedabad.
Meteorological Department, by providing Cyclone Surveillance Radars at Calcutta in the east coast and at Goa, Bombay in the west coast.
Satellite picture receiving equipments at Delhi, Bombay, Madras are receiving satellite pictures of the cyclones from the polar-orbiting Satellites of the U.S.A. and U.S.S.R. Since April 1982.
A.V.H.R.R. (Advance very High Resolution Radio-meter) Indian GeoStationary Satellite INSAT-LB has become operational since October 1983. Monitoring of the cyclone by taking hourly pictures has helped the forecaster to improve his skill in issuing the timely warnings to the public.

## Slide 98: Cyclone Monitoring Satellites
providing weather forecasting, cyclone
SATCAT no. SCATSAT-1 (Scatterometer Satellite-1) is a
prediction, and
satellite tracking
services to India.
It has been developed by ISRO Satellite Centre, Bangalore whereas its payload was developed by Space Applications Centre, Ahmedabad.

## Slide 99: SOME INDIAN ASSOCITIONS
Area Cyclone Warning Centres (ACWC)
Cyclone Warning Centres (CWC)
Numerical Weather Prediction (NWP)
Northern Hemispheric Analysis Centre (NHAC)
Cyclone Warning Research Centre (CWRC)
Regional Specialized Meteorological Centre

## Slide 100: National Level Disaster Prevention Team
The Team of Govt. of India establish in 1969,set up "Cyclone Distress Mitigation Committee" (CDMC) with the objective of preventing loss of life and minimizing damage to properties.

## Slide 102: Tsunami
A Tsunami also known as seismic sea wave, it is a series of water waves caused by displacement of a large volume of a body of water, generally an ocean or a large lake. Tsunami waves do not resemble normal sea waves as their wavelength is longer. Rather than appearing as a breaking wave. A tsunami may initially resembles a rapidly rising tide & for this reason tsunamis are often referred to as tidal waves.

## Slide 103: How are tsunamis generated?
Tsunamis are generated by any large, impulsive displacement of the sea bed level.
Earthquakes generate tsunamis by vertical movement of the sea floor. If the sea floor movement is horizontal, a tsunami is not generated. Earthquakes of M > 6.5 are critical for tsunami generation.
Tsunamis are also triggered by landslides into or under the water surface, and can be generated by volcanic activity and meteorite impacts.

## Slide 104: How often do tsunamis occur?
On the average, there are two tsunamis per year in the Pacific Ocean somewhere, which cause damage near the source.
Approximately every 15 years a destructive tsunami occurs in Pacific.
The destructive tsunami on Dec 26th, 2004 on the Indian Coast in terms of its impact seems to have occurred for the first time in the history.

## Slide 105: How fast does a tsunami travel?
Tsunami velocity is dependent on the depth of water through which it travels (Velocity equals the square root of water depth h times the gravitational acceleration g, that is V =√g h).
Tsunamis travel approximately at a velocity of 700 kmph in 4000 m depth of sea water. In 10 m of water depth the velocity drops to about 36 kmph.

## Slide 106: Tsunamis in India

## Slide 107: Tsunami risk
TSUNAMI RISK = TSUNAMI HAZARD * EXPOSURE * VULNERABILITY.
Tsunami Hazard assessment: • Preparation of data-base of historical and archival information of relevant Indian Tsunamis, with the emphasis clearly on the December 26, 2004 event. • Supplement the data from computer based simulations. • Analyses of these data, to -define the scenario Tsunamis from various earthquake sources -prepare the Tsunami hazard map.
Exposure: • List all habitations below 10 m contour level and locate on a map. • List and locate all vital installations below 10 m contour level.
VULNERABILITY assessment: • Based on the earthquake vulnerability assessment, define the vulnerability of various exposed elements on the coastal, island and reef environments and in the Ports and Harbours • Prepare vulnerability maps (based on Remote Sensing, Geographical information system and other data related to various hazards).

## Slide 108: Key factors to reduce potential losses due to tsunami
1 Building Codes (potential damage due to wave action and flooding)
GIS Mapping
Land-Use Planning (taking note of wave action & flooding)
Disaster Planning (in identified hazard zones)
Emergency Management
Emergency Personnel Training (necessary aspects relevant to marine situations)
Rescue and Response (marine situations related to shipping) (cargo, tourist, inter-islands fishing community, recreational boating)
Insurance Needs
Community Education
Simulated Tsunami Exercises

## Slide 109: Measures for safety from Tsunamis
Structural Measures
Construction of cyclone shelters
Plantation of mangroves and coastal forests along the coast line
Development of a network of local knowledge centers (rural/urban) along the coast
lines to provide necessary training and emergency communication during crisis time
Construction of location specific sea walls and coral reefs in consultation with experts
Development of well designed break waters along the coast to provide necessary
cushion against cyclone and tsunami hazards
Development of tsunami detection, forecasting and warning dissemination centres
Development of a “Bio-Shield” - a narrow strip of land along coastline.
Identification of vulnerable structures and appropriate retrofitting for tsunami/cyclone resistance of all such buildings as well as appropriate planning, designing, construction of new facilities.

## Slide 110: Measures for safety from Tsunamis
Non-structural Measures
Strict implementation of the coastal zone regulations (within 500 m of the high tide line
with elevation of less than 10 m above mean sea level).
Mapping the coastal area for multiple hazards, vulnerability and risk analysis upto taluka
/village level. Development of Disaster Information Management System (DIMS) in all the
coastal states.
Aggressive capacity building requirements for the local people and the administration for
facing the disasters in wake of tsunami and cyclone, ‘based on cutting edge level’
Developing tools and techniques for risk transfer in highly vulnerable areas
Launching a series of public awareness campaign throughout the coastal area by various means including AIR, Doordarshan & Other Media.
Training of local administration in forecasting warning dissemination and evacuation techniques
Awareness generation and training among the fishermen, coast guards, officials from fisheries department and port authorities and local district officials etc., in connection with evacuation and post tsunami storm surge management activities. Regular drills should be conducted to test the efficacy of the DM plans.
Studies focusing on the tsunami risk in India may be taken under NCRM project.

## Slide 111: The Present status of Tsunami Warnings in India.
Tsunami is very low probability event in India. As such, there are no Codal provisions for
Tsunami warnings in India as yet though; there is a good seismological network in India to record any earthquake within the country and its neighborhood.
The need of a Tsunami Warning Centre (TWC) in India is now being conceptualized at the
Government of India level.
Indian Meteorological Department (IMD), is working on a proposal to set up a real time
earthquake monitoring system in India.
The Department of Ocean Development in collaboration with Departments of Space and IMD
under Department of Science and Technology is evolving a plan of tsunami warning system in
the Bay of Bengal and the Arabian Sea.
The data from observing points to Warning Centre(s) will be sent through satellite links. Specific
systems called Deep Ocean Assessment and Reporting of Tsunamis (DART) using Bottom
Pressure Recorder, acoustic modem, acoustic release system, battery pack bolted to platform
and float action and recovery aids will be deployed.
The warning centres in the Indian context could be the Emergency Operation Centre at the
State & District level, which are being designed to function round the clock under the District
Collector at District level and under the Chief Minister at State level.

## Slide 112: Heat Wave
A heat wave
is a prolonged period of excessively hot weather accompanied by high humidity, especially in oceanic climate
countries, a heat wave is measured relative to the usual weather in the area & relative to normal temperatures for the season, heat wave is considered extreme weather & a danger because heat & sunlight may damage the Human body.

## Slide 113: Health Impacts of Heat Waves
The health impacts of Heat Waves typically involve dehydration, heat cramps, heat exhaustion and/or heat stroke. The signs and symptoms are as follows:
Heat Cramps: Ederna (swelling) and Syncope (Fainting) generally accompanied by fever below 39oC i.e. 102oF.
Heat Exhaustion: Fatigue, weakness, dizziness, headache, nausea, vomiting, muscle cramps and sweating.
Heat Stoke: Body temperatures of 40oC i.e. 104oF or more along with delirium, seizures or coma. This is a potential fatal condition

## Slide 114: Climate Change -Global warming, Sea level rise, ozone depletion
Climate Change is the defining issue of our time and we are at a defining moment.
From shifting weather patterns that threaten food production, to rising sea levels that increase the risk of catastrophic flooding, the impacts of climate change are global in scope and unprecedented in scale.
Without drastic action today, adapting to these impacts in the future will be more difficult and costly.

## Slide 115: Global warming
The earth’s atmosphere has always acted like a greenhouse to capture the sun’s heat, ensuring that the earth has enjoyed temperatures that permitted the emergence of life forms as we know them, including humans.
Global warming is the slow increase in the average temperature of the earth’s atmosphere because an increased amount of the energy (heat) striking the earth from the sun is being trapped in the atmosphere and not radiated out into space.

## Slide 116: How does Global Warming drive Climate Change?
Heat is energy and when you add energy to any system changes occur.
Because all systems in the global climate system are connected, adding heat energy causes the global climate as a whole to change.
Much of the world is covered with ocean which heats up. When the ocean heats up, more water evaporates into clouds.
Where storms like hurricanes and typhoons are forming, the result is more energy-intensive storms. A warmer atmosphere makes glaciers and mountain snow packs, the Polar ice cap, and the great ice shield jutting off of Antarctica melt raising sea levels.
Changes in temperature change the great patterns of wind that bring the monsoons in Asia and rain and snow around the world, making drought and unpredictable weather more common.
116

## Slide 117
Causes of Global Warming
That global warming is occurring as a result primarily of human activity and so climate change is also the result of human activity.

## Slide 118: The most important greenhouse gases(GHGs)
CO2 or carbon dioxide is produced any time something is burned. It is the most common
GHG, constituting by some measures almost 55% of total long-term GHGs.
Methane or CH4 is produced in many combustion processes and also by anaerobic decomposition. Methane breaks down in approximately 10 years, but is a precursor of ozone, itself an important GHG.
Nitrous oxide in parean (laughing gas), is a byproduct of fertilizer production and use, other industrial processes and the combustion of certain materials. Nitrous oxide lasts a very long time in the atmosphere, but at the 100 year point.
Fluorinated gases were created as replacements for ozone depleting refrigerants, but have proved to be both extremely long lasting and extremely warming GHGs. They have no natural sources, but are entirely man-made. At the 100 year point of comparison
Sulphur hexafluoride or SF6 is used for specialized medical procedures, but primarily in what are called dielectric materials, especially dielectric liquids. These are used as insulators in high voltage applications such as transformers and grid switching gear. SF6 will last thousands of years in the upper atmosphere.

## Slide 119: Sea-level Rise
Climate change impacts rising sea levels. Average sea level around the
world rose about 8 inches (20 cm) in the past 100 years; climate scientists
expect it to rise more and more rapidly in the next 100 years as part of climate change impacts.
Coastal cities such as New York are already seeing an increased number of
flooding events and by 2050 many such cities may require seawalls to
survive. Estimates vary, but conservatively sea levels are expected to rise 1
to 4 feet (30 to 100 cm), enough to flood many small Pacific island states
(Vanatu), famous beach resorts (Hilton Head) and coastal cities (Bangkok, Boston).
If the Greenland ice cap and/or the Antarctic ice shelf collapses, sea levels
could rise by as much as 20 ft (6 m), inundating, for example, large parts of Florida, the Gulf Coast, New Orleans and Houston.

## Slide 120: Ozone depletion
Atmospheric ozone absorbs ultraviolet (UV) radiation from the sun, particularly harmful UVB-type rays. Exposure to UVB radiation is linked with increased risk of skin cancer and cataracts, as well as damage to plants and marine ecosystems.
Ozone, on the other hand, consists of three atoms of oxygen bound together (O3).
Most of the atmosphere's ozone occurs in the region called the stratosphere. Ozone is colourless and has a very harsh odour.

## Slide 121: Ozone at different levels
Ozone also occurs in very small amounts in the lowest few kilometres of the atmosphere, a region known as the troposphere.
It is produced at ground level through a reaction between sunlight and volatile organic compounds (VOCs) and nitrogen oxides (NOx), some of which are produced by human activities such as driving cars.
Stratospheric ozone blocks harmful solar radiation - all life on Earth has adapted to this filtered solar radiation.
Ground-level ozone, in contrast, is simply a pollutant. It will absorb some incoming solar radiation, but it cannot make up for ozone losses in the stratosphere.

## Slide 122: Ozone Hole
Frequently, the term is employed to describe ozone depletion.
Technically, the term "ozone hole" should be applied to regions where stratospheric ozone depletion is so severe that levels fall below 200 Dobson Units (D.U.), the traditional measure of stratospheric ozone.
Normal ozone concentration is about 300 to 350 D.U [3]. Such ozone loss now occurs every springtime above Antarctica, and to a lesser extent the Arctic, where special meteorological conditions and very low air temperatures accelerate and enhance the destruction of ozone loss by man-made ozone depleting chemicals (ODCs).

## Slide 123: EFFECTS OF OZONE DEPLETION
Effects on Human and Animal Health
Effects on Terrestrial Plants
Effects on Aquatic Ecosystems
Effects on Bio-geo-chemical Cycles
Effects on Air Quality
Effects on Materials
Effects on Climate Change
Effects on Ultraviolet Radiation

## Slide 124: INTERNATIONAL ACTIONS
Montreal Protocol - On the basis of the Vienna Convention, the Montreal Protocol on Substances
that Deplete the Ozone Layer was negotiated and signed by 24 countries and by the European
Economic Community in September 1987. The Protocol called for the Parties to phase down the use of CFCs, halons and other man-made ODCs.
Australian Chlorofluorocarbon Management Strategy - It provides a framework for the
responsible management and use of CFCs in Australia. The strategy recognizes some continuing
need for these chemicals in pharmaceutical and laboratory uses, but commits to their gradual phasing out.
Environmental Protection (Ozone Protection) Policy2000 - This WA policy aims to minimize the discharge of ozone-depleting substances into the environment, and has been extended to cover use of alternative refrigerants (where relevant).
United Nations Environment Programme - Has published several assessments of the environmental effects of ozone depletion (United Nations Environment Programme, 1998; World Meteorological Organization, 2002)
Ozone Protection and Synthetic Greenhouse Gas Management Act 1989 (and associated regulations and amendments) - Was implemented by the Commonwealth Government to meet its commitments under the Montreal Protocol.
Ultraviolet index forecast - The Bureau of Meteorology has developed a model to predict the amount of ultraviolet exposure and the times of day at which it will occur for 45 WA locations. It is designed to help people minimize their exposure to dangerous levels of ultraviolet radiation.

## Slide 125
END